## Slide 1: Ender-5 S1
3D Printer User Manual
V1.3
Ender-5 S1
Create reality，achieve dreams

## Slide 2
To Our Dear Users
Thank you for choosing Creality. To make using our products easier, please read this User Manual before you start and follow the instructions provided carefully.
Creality is always ready to provide you with high-quality services. If you encounter any issues or have any questions when using our products, please use the contact information at the end of this manual to contact us.
To further improve your user experience, you can ﬁnd more about our devices via the following methods: User manual: You can ﬁnd instructions and videos in the SD card provided with the printer.
You can also visit our oﬃcial website (https://www.creality.com) to ﬁnd information regarding software, hardware, contact information, device instructions, device warranty information, and more.
Firmware Upgrade
Please visit our oﬃcial website https://www.creality.com/download, switch to your language, then select your printer and model. Download the required ﬁrmware and install it to use it with your printer.

## Slide 3
Instructions for Use
Do not use this printer by methods or operations not described in this manual, otherwise it may result in accidental injury or property damage.;
Do not place this printer near ﬂammable materials, explosive materials or high heat sources. Please place this printer in a ventilated, cool and low-dust environment.
Do not place this printer in a vibrating or any other unstable environment, as the printing quality will be compromised when the printer shakes.
Please use the ﬁlament recommended by the manufacturer, otherwise the nozzle may be clogged or the printer may be damaged.
Please use the power cord provided with the printer and do not use the power cord of other products. The power plug must be plugged into a three-hole socket with a ground wire.
Do not touch the nozzle, hotbed or motor while the printer is in operation, otherwise you may get burned.
Do not wear gloves or accessories while operating the printer, otherwise the moving parts may cause accidental injury including cuts and lacerations.
After the printing process is complete, please use tools to clean up the ﬁlament on the nozzle while the nozzle is still hot. Do not touch the nozzle with your hands when cleaning, otherwise your hands may get burned.
Clean the printer frequently. Always turn the power oﬀ when cleaning, and wipe with a dry cloth to remove dust, adhered printing plastics or any o ther material oﬀ the frame,guide rails, or wheels. Use glass cleaner or isopropyl alcohol to clean the print surface
Children under the age of 10 must not use this printer without adult supervision in order to avoid accidental injury.
This printer has a safety protection mechanism. Please do not manually move the nozzle or printing platform quickly while the printer is on, otherwise the printer will automatically power oﬀ for protection.
Users should abide by the laws and regulations of the country and region where the equipment is located (place of use), abide by professional ethics, and pay attention to safety obligations. It is strictly forbidden to use our products or equipment for any illegal purpose. Our company is not responsible for the relevant legal responsibilities of any violators.

## Slide 10
5. Assembling 3D Printer
5.2 Install the Top Component
A. Place the top component on top of the proﬁle and pre-lock each of the four corners with No.25 screws before locking them all.
25
25 M5×25 Hexagon Socket
Head Cap Screw with Spring Washer × 8
06

## Slide 11
5. Assembling 3D Printer
5.3 Install the Z-axis Kit
A. Put the print platform component on the foam support and combine it with the Z-axis component to form a Z-axis kit, then fasten it with the No.25 screws.
Z axis motor
25
Tips: The foam in the box can be used as a support.
25 M5×25 Hexagon Socket Head Cap Screw with Spring Washer × 4
07

## Slide 12
Tips: ① Platform L support assembly: L support + support block;
② Platform R support assembly: R support + support block
27
26
Socket Head Cap Screw × 4
Socket Head Cap Screw × 2
26 M5×25 Hexagon 27 M5×20 Hexagon
5. Assembling 3D Printer
5.3 Install the Z-axis kit
Place the Z-axis assembly upside down on the foam support, then ﬁx the platform support to the linear bearing, and lock it with No.26 screws;
Secure the other end of the platform support to the proﬁle using No.27 screws to lock it in place.
Z axis motor
①
②
08

## Slide 13
5. Assembling 3D Printer
5.3 Install the Z-axis Kit
A. Tilt the Z-axis kit while placing the bottom inside the equipment frame proﬁle.
09

## Slide 14
5. Assembling 3D Printer
5.3 Install the X-axis Kit
Hold the frame at an angle, push the Z-axis kit in and lift it between the top proﬁle and the optical axis;
Be sure that the bottom optical axis holder is located on the proﬁle.
The optical axis holder is to be clamped on the proﬁle
Be placed between the top proﬁle and the optical axis

## Slide 15
5. Assembling 3D Printer
5.3 Install the Z-axis Kit
A. Align the top of the Z-axis kit with the proﬁle holes, pre-lock it ﬁrst with the No.24 screws and then tighten all the screws.
24
24 M5×30 Hexagon Socket Head Cap Screw with S pring Washer × 4

## Slide 16
5. Assembling 3D Printer
5.4 Install the Diagonal Bracing
A. Put two diﬀerent diagonal bracing on the bottom of the proﬁle and lock the ends to the proﬁle using No.27 screws.
27
8
Diagonal bracing
27 M5×20 Hexagon Socket Head Cap
Screw × 4

## Slide 17
5. Assembling 3D Printer
5.5 Install the Material Rack
A. After assembling and tightening the material barrel and bracket into a material rack, use the No.28 screws to secure and lock it to the proﬁle.
28
28 M5×14 Hexagon Socket Button Head Screw × 2
13

## Slide 18
5. Assembling 3D Printer
5.6 Equipment Wiring
X axis motor
Y
Y
E.Connect the Z-axis motor cable to the Z-axis limit switch cable
Z
D.Connect the Y-axis motor cable to the Y-axis limit switch cable
Z
X
X
A.Connect the X-axis motor cable to the X-axis limit switch cable
B.Connect the ﬁlament detection line;
D
Y axis motor
Z axis motor
F.Connect the hotbed cable
C.Connect the Extruder Kit line

## Slide 19
5. Assembling 3D Printer
5.7 Install the Teﬂon Tube
A. Insert one end of the Teﬂon tube into the interface of the Teﬂon tube ﬁxing block,
with the other end inserted through the snap to the bottom and ﬁnally into the blue jaws.

## Slide 20
5. Assembling 3D Printer
5.8 Fix the ﬂexible ﬂat cable
A. To maintain a smooth alignment, please use ﬂat cable clips and cable ties to secure the ﬂat cables to the proﬁle as shown in the diagram to avoid abnormal compression caused by printing interference and tangling during the operation of the device.
Bending harnesses
Cable Tie
Flexible Flat Cable Clip × 5
Bending Harnesses

## Slide 21
Using the 3D Printer
  Switch on the Power
A. Please select the correct voltage mode according to the local grid voltage and then switch on the power.
Please ensure the correct position for the power supply switch and mains before supply connection, in order to avoid damage to the device.
Caution: ● If the mains between 100V and 120V, please select the 115V for the power supply switch.
If the mains between 200V and 240V, please select the 230V for the power supply switch (default is 230V).
115V
230V

## Slide 22
6.Using the 3D Printer
6.2 Auxiliary Leveling
A. Click on "Settings" and go to "Leveling Method";
B. Click on "Z-axis Homing" ﬁrst, and then adjust the Z-axis compensation value when the nozzle returns to the center of the platform, to ensure that the nozzle is approximately 0.1mm from the platform, about the thickness of a piece of an A4 paper.
>>

## Slide 23
6.Using the 3D Printer
6.2 Auxiliary Leveling
A. Click on the numbers 2, 3, 4 and 5 on the screen respectively to move the nozzle to the corresponding position, turn the leveling nut and adjust the printing platform so that it is in just the right position to ﬁt the nozzle with a spacing of approximately 0.1mm; then level the four corners in sequence.
Tips: You can use a standard leveling card or a piece of A4 paper to aid leveling so that the nozzle just makes a scratch on the A4 paper; adjust the four leveling nuts in turn, and make continuous adjustments until you can feel a slight resistance from the nozzle when pulling on the A4 paper.
The nozzle is too far away from the platform, and the ﬁlaments cannot stick to the platform.
Filaments are extruded evenly, just sticking on the platform.
The nozzle is too close to the platform, leading to insuﬁcient ﬁlament extrusion, even scraping the platform.

## Slide 24
6.Using the 3D Printer
6.3 Auto Leveling
A. Click on "Settings", go to "Leveling Method", select "AUTO. LVL" and click on the "Start" button to start automatic leveling.
B. Until auto leveling is 100% completed.
>>

## Slide 25
6.Using the 3D Printer
6.4 Printer Preheating
A. Manual Temperature Setting: Select "Prepare", click on "Temperature Setting" and then manually set the temperature of the nozzle and hotbed based on the ﬁlaments used for printing.
>>
>>

## Slide 26
6.Using the 3D Printer
6.4 Printer Preheating
A. Auto Temperature Setting: select "Prepare", click on "Temperature Setting" and select "Preheat PLA" or "Preheat ABS" to preheat the nozzle and hotbed based on the material to be printed.
Tips: 1、PLA Preheating Temperature: nozzle temperature 205°, hotbed temperature 60°; ABS preheating temperature:
nozzle temperature 260°, hotbed temperature 90°.
2、When changing the ﬁlaments, if you need to heat the nozzle, pull out the ﬁlaments quickly after they have melted to avoid the cool-down of the melted ﬁlaments in the nozzle above the heat break.
3、If the ﬁlaments are pulled out directly without heating the nozzle, some of the ﬁlaments may be left in the nozzle, resulting in clogging or even damage to the extruder.
>>

## Slide 27
6.Using the 3D Printer
6.5 Filament Loading
A. Cut and straighten the front end of the ﬁlament at 45 degrees and place the tray on the material rack.
Tips: How to Replace the Filament?
Method 1. Withdraw the ﬁlaments quickly and feed the new ﬁlaments after the nozzle is preheated and ﬁlaments are pushed a little forward. Method 2. Cut ﬁlaments near the extruder and slowly feed new ﬁlaments until they are fed into the material barrel.

## Slide 28
>>
>>
B.Go to Select language → Next → Select model → Next → Finish to complete the conﬁguration.
A. Visit our oﬃcial website (https://www.creality.com) to download and install the software, or install the Creality software via the memory card provided with the printer.
6.Using the 3D Printer
6.6 Start Printing
>>
Creality
Slicer 4.8.2
Creality
Slicer 4.8.2
C.Launch the Creality slicing software → Load → Select the ﬁle.
Creality Slicer 4.8.2
>>
>>

## Slide 29
E.Insert the memory card.
D.Generate the G-code ﬁle → Save it to the memory card.
>>
6.Using the 3D Printer
6.6 Start Printing
Note:
For details on using the software, please refer to the slicing software user manual on the memory card.
Saved ﬁles must be placed in the root directory (not a subdirectory) of the memory card.
The ﬁle name must be Latin letters or numbers, not Chinese characters or other special symbols, and no more than 20 characters.
Do not insert or remove the memory card during the printing process.

## Slide 30
>>
>>
B. Click on the Start Printing button;
C. Already in printing status.
A. Choose the ﬁle to be printed;
6.Using the 3D Printer
6.6 Start Printing

## Slide 31
Maintenance Instructions
  Platform Plate Maintenance
A. If there are residual ﬁlaments on the platform plate,
scrape them oﬀ lightly with a blade and print again.
7.2 Nozzle Replacement
B. If the ﬁrst layer of the model is not properly glued, it is recommended to apply
solid adhesive evenly on the surface of the platform plate before preheating for printing.
A. Remove the silicone protective cover;
B. Remove the old nozzle;
C. Mount a new nozzle;
D. Mount the silicone protective cover.
Warnings:
If there are ﬁlaments inside the nozzle, it is necessary to preheat the nozzle when replacing it;
Prevent scalding when replacing nozzles which are hot;
Use a tool to hold the heating block in place when removing the nozzle to avoid damage to the components.

## Slide 32
7.Maintenance Instructions
7.3 Lubrication Protection
A. You are recommended to purchase your own lubricating ﬂuid for regular maintenance of the optical axis area.

## Slide 33
7.Maintenance Instructions
7.4 Error Code Instructions
No. Error Code Instructions |  | Parameters
1 | E06 | Hotend Thermal Runaway!
2 | E07 | Hotend Heating Failed!
3 | E08 | Hotend Thermistor Error!
4 | E09 | Hotbed Thermal Runaway!
5 | E10 | Hotbed Heating Failed!
6 | E11 | Hotbed Thermistor Error!
7 | E201 | Timeout
8 | E202 | Homing Failed
9 | E203 | Probing Failed
10 | E204 | Click Reboot
In the event that any of the above problems arise and cannot be resolved: ① Please visit https://www.crealitycloud.com/product, click “Products" and select the right model, and then click “Related" to view the tutorials on after-sales service; ② Or contact our after-sales service center at +86 755 3396 5666, or send e-mail to cs@creality.com. |  |